## Slide 1: CAM, Module 2
Melvin C Jose
ECE ,VJCET

## Slide 2: SYLLABUS
Module 2: 8051 Architecture Microcontrollers and Embedded Processors. Architecture – Block diagram of 8051, Pin configuration, Registers, Internal Memory, Timers, Port Structures, Interrupts. Assembly Language Programming - Addressing Modes, Instruction set (Detailed study of 8051 instruction set is required).

## Slide 3: 8051- Features
8 bit microcontroller with 8 bit wide data bus
4 Kb of internal ROM for program storage
128 bytes of internal RAM
4 ports having a total of 32 input/output pins
Maximum addressing capacity 64k (16 bit address bus)
Two 16 bit timer/counters
Full duplex serial data receiver/transmitter
Two external and three internal interrupts

## Slide 6: 8051 Architecture
ALU: Performs arithmetic and logic operations like addition, subtraction, AND , OR etc.
CPU registers : A and B
A –accumulator
  • 8 bit
  • Used in all ALU operations
  • Used for all data transfer between 8051 and external memory

## Slide 7: 8051 Architecture
B Register
  • 8 bit
  • Used for division and multiplication operations
  • Also used for 8 bit data storage when not used by multiplication and division instructions
Program counter and Data pointer
  • 16 bit registers
  • Holds 16 bit address

## Slide 8: 8051 Architecture
PC
  Stores the address of the next instruction to be executed
  Automatically incremented after each instruction fetch
  Does not have an internal address
  Default value 0000h
DPTR
  Made of two 8 bit registers DPH and DPL
  Used for external memory access (code and data)

## Slide 9: 8051 Architecture
PSW

## Slide 10: PSW
CY- Carry Flag: This flag is set if there is a carry out from the D7 bit. This flag is affected by addition and subtraction operations and instructions that set or clear it directly.
AC- Auxiliary Carry Flag: This flag is set if there is a carry out from the D3 to D4; otherwise it is cleared. It is used for BCD operations
F0- User Flag 0- User defined flag
RS1- Register bank select bit 1
RS0- Register bank select bit 0

## Slide 11: PSW
RS1 | RS0 | Register Bank Status
0 | 0 | Select register Bank 0 (00H-07H)
0 | 1 | Select register Bank 1(08H-0FH)
1 | 0 | Select register Bank 2 (10H-17H)
1 | 1 | Select register Bank 3 (18H-1FH)
These bits are used to select the current register bank from among the 4 register banks of 8051. Their default value is 00 ie Bank0 is the default register bank.

## Slide 12: Register Banks
https://srinivas4706.blogspot.com/2019/02/unit-ii-microcontroller-notes.html

## Slide 13: PSW
OV- overflow flag: This flag is set if there is an overflow into the sign bit. This occurs when the result of a signed operation is too large causing the higher order bit to overflow into the sign bit.
P- Parity Flag: If the accumulator contains odd number of 1s then P=1 else P=0
  • All flags can be set or cleared by user
  • Math flags-C,AC,OV and P- are also affected by ALU operations
  • Of the three general purpose flags F0 is placed in the PSW and GF0 and GF1 are placed in PCON

## Slide 14: STACK AND STACK POINTER
Stack is a part of internal RAM used to store and retrieve data quickly
LIFO – stack operates in last in first out manner
Stack grows up as data is stored
Stack pointer is an 8 bit register which holds the address of top of stack
Default value of SP is 07
Value of SP can be changed to any internal RAM address
PUSH and POP instructions are used to store and retrieve data

## Slide 22: 8051 Architecture
ROM
  4 kb internal ROM for program storage
RAM
  128 bytes Internal RAM
1. Register banks-32 bytes
  Organized as 4 register banks
  Each register bank contains 8 registers –R0 to R7
2. Bit addressable memory-16 bytes
  128 bits
  May be addressed by bit address or by byte address(as 8 bits)
3. General Purpose (scratch pad) RAM-80 bytes
  Byte addressable

## Slide 23: 8051 Architecture
TIMERS
  Two sixteen bit timers
  May be programmed to count internal clock pulses- timer or external clock pulses- counter
I/O PORTS
  32 i/o pins arranged as four 8-bit ports
SERIAL I/O
  Full duplex serial data receiver transmitter

## Slide 24: 8051 Architecture
INTERRUPTS
  2 external and 3 internal interrupts
  External interrupts- INT0 , INT1
  Internal interrupts- timer0, timer1 and serial communication
OSCILLATOR AND CLOCK
  All internal operations are synchronized with clock
  Quartz crystal and capacitors are used to form the resonant network that generates clock

## Slide 25: Memory Organization
4Kb of internal ROM (Program Memory )
  ROM is used to permanently save the program being executed
128 bytes of internal RAM
    Data Memory (RAM) is used for temporarily storing data and intermediate results created
  8051 microcontrollers have a 16-bit address bus and are capable of addressing 64 kb of external memory.

## Slide 26: ROM /Program Memory
8051 has 4 kb internal ROM and expanded 64 kb of external ROM.
Internal ROM occupies the program memory space from 0000h to 0FFFh.
Program addresses higher than 0FFFh are automatically accessed from external memory if total program size exceeds 4K.
Program is fetched entirely from external memory if EA/VPP pin is grounded. (In this case addresses from 0000h to FFFFh are in external memory)

## Slide 27: ROM /Program Memory

## Slide 28: RAM/Data Memory
Internal RAM
8051 has 128 bytes of internal RAM having addresses from 00h to 7F h.
It is organized into 3 regions
1. Register banks-32 bytes- 00h to 1Fh
2. Bit addressable memory-16 bytes- 20h to 2Fh
3.General Purpose (scratch pad) RAM-80 bytes- 30h to 7Fh

## Slide 30: RAM/Data Memory
Register banks-32 bytes- 00h to 1Fh
Organized as 4 register banks
  Each register bank contains 8 registers –R0 to R7
  Registers may be addressed by name or by internal RAM address
  RS0 and RS1 of PSW determine which bank is currently in use
  Default bank is bank0

## Slide 31: RAM/Data Memory
2.Bit addressable memory-16 bytes- 20h to 2Fh
128 bits
  May be addressed by bit address or by byte address(as 8 bits)
  Eg :Individual bits of the byte with byte address 20h can addressed using bit addresses 00h to 07h
3.General Purpose (scratch pad) RAM-80 bytes- 30h to 7Fh
  Byte addressable

## Slide 32: Special Function registers
SFR registers uses the address range of 80h through FFh.
21 Special function registers (SFR) in 8051 micro controller
It includes Register A, Register B, Program Status Word (PSW), PCON etc. Each SFR has an address (80h through FFh) and a name.
Example: the accumulator having the address 0E0h.
Note : All addresses from 80 to FF are not used for SFRs; attempting to use an address that is not defined yields unpredictable results

## Slide 33: External RAM
External RAM up to 64 K can be added to 8051. It is accessed using DPTR.

## Slide 34: Registers

## Slide 35: Registers

## Slide 36: Register A/Accumulator
Accumulator which is also known as ACC or A is the most important of all special function registers.
It holds one of the operands and the result of most arithmetic and logic operations.
ACC can be accessed by direct addressing.
To access accumulator as a single byte (all 8 bits at once) the physical address E0H can be used.

## Slide 37: Register A/Accumulator
Accumulator is both byte and bit addressable.
To access the first bit (i.e bit 0) use the physical address E0H or Acc.0 .
To access the second bit (i.e bit 1), E1H or Acc.1
For third bit E2H or Acc.2 and so on.

## Slide 38: Register A/Accumulator

## Slide 39: Register B
Register B holds the multiplier during multiplication and divisor during division.
Register B is also byte and bit addressable.
To access all 8 bits (as a single byte), physical address F0 is used.
To access bit 0, F0 or B.0 is used. To access bit 1 you may use F1or B.1 and so on.
Register B can also be used for other general purpose operations.

## Slide 40: Register B

## Slide 41: Port Registers
8051 has 4 I/O ports named P0, P1, P2 and P3.
Each port has got a corresponding port register with the same name.
Data must be written into port registers first to send it out to any other external device through ports.
Similarly any data received through ports must be read from port registers.
All 4 port registers are bit as well as byte addressable.

## Slide 42: Port Registers

## Slide 43: Port Registers
The physical addresses of the port registers are : P0-80h, P1-90h, P2-A0h and P3- B0h

## Slide 44: Stack Pointer
Stack pointer is an 8 bit register which points to the last stored location of the stack.
Before storing a byte in stack, the SP is incremented by 1.
After a system reset SP is initialized to the default value 07H
Data can be stored to stack from 08H onwards.
The programmer can alter the value of SP if required.

## Slide 45: Data Pointer
The Data Pointer (DPTR) is a user-accessible 16-bit register used by the 8051 to access external memory.
It can also be used to store 16 bit values.
It is a combination of two 8 bit registers DPH and DPL
which can be accessed independent

## Slide 46: Data Pointer

## Slide 47: Power Management Register (PCON)
Power management using a microcontroller is something you see every day in mobile phones.
Example : A mobile phone automatically going into stand by mode when not used for a couple of seconds or minutes
Commonly referred to as PCON register, this is a dedicated SFR for power management alone.

## Slide 48: Power Management Register (PCON)
From the figure below you can observe that there are 2 modes for this register :- Idle mode and Power down mode

## Slide 50: Idle Mode
Idle mode is entered by setting IDL bit to 1 .
The clock signal is gated off to CPU, but not to the interrupt, timer and serial port functions.
The CPU status is preserved entirely. SP, PC, PSW, Accumulator and other registers maintain their data during IDLE mode. The port pins hold their logical states they had at the time Idle was initiated. ALE and are held at logic high levels.

## Slide 51: Idle Mode
Ways to exit Idle Mode:
Activation of any enabled interrupt will clear PCON.0 bit and hence the Idle Mode is exited.
The program goes to the Interrupt Service Routine (ISR). After RETI is executed at the end of the ISR, the next instruction will start from the one following the instruction that enabled Idle Mode.
A hardware reset exits the idle mode. The CPU starts from the instruction following the instruction that invoked the 'Idle' mode.

## Slide 52: Power Down Mode
The Power down Mode is entered by setting the PD bit to 1.
The internal clock to the entire microcontroller is stopped (frozen). However, the program is not dead.
The Power down Mode is exited (PCON.1 is cleared to 0) by Hardware Reset only.
The CPU starts from the next instruction where the Power down Mode was invoked.
Port values are not changed/ overwritten in power down mode.
Vcc can be reduced to as low as 2V in Power down mode. However, Vcc has to be restored to normal value before Power down mode is exited.

## Slide 53: Processor Status Word (PSW)

## Slide 54: Processor Status Word (PSW)

## Slide 55: Processor Status Word (PSW)

## Slide 56: SFR
There are 21 SFR’s ,we have discussed only 9 specifically.
The table below lists all other 12 SFR’s

## Slide 57: SFR

## Slide 58: SFR

## Slide 60: Timer Registers

## Slide 62: TCON Registers

## Slide 65: Interrupt Enable Register

## Slide 66: Interrupt Priority Register

## Slide 67: SCON Register

## Slide 69: Pin Diagram

## Slide 70
Pins 1-8: Port 1 :Each of these pins can be configured as an input or an output.
Pin 9: RST : a HIGH on this pin resets the microcontroller. The program starts execution from 0000h. All internal registers are reset to default values.
Pins10-17: Port 3 Similar to port 1, each of these pins can serve as general input or output. Besides, all of them have alternative functions:
Pin 10: RXD Serial communication input
Pin 11: TXD Serial communication output

## Slide 71
Pin 12: INT0 External Interrupt 0 input.
Pin 13: INT1 External Interrupt 1 input.
Pin 14: T0 Timer 0 external clock input.
Pin 15: T1 Timer 1 external clock input.
Pin 16: WR External Data memory write control signal
Pin 17: RD External data memory read control signal.
Pin 18, 19: XTAL2 , XTAL1 . A quartz crystal which specifies operating frequency is usually connected to these pins.
Pin 20: VSS or GND Ground.

## Slide 72
Pin 21-28: Port 2 If there is no intention to use external memory then these port pins are configured as general inputs/outputs. In case external memory is used, the higher address byte, i.e. addresses A8-A15 will appear on this port.
Pin 29: PSEN Program Store Enable: If external ROM is used for storing program then the microcontroller reads a byte from memory whenever a logic zero (0) appears on it. This pin is usually connected to the OE –output enable pin of external ROM.

## Slide 73
Pin 30: ALE/PROG-Address Latch Enable : Prior to reading from external memory, the microcontroller puts the lower address byte (A0-A7) on P0 and activates the ALE output. After receiving signal from the ALE pin, the external register (usually 74HCT373 or 74HCT375 add-on chip) latches the state of P0 and uses it as a memory chip address. Immediately after that, the ALU pin is returned to its previous logic state and P0 is now used as a Data Bus.

## Slide 74
Pin 31: EA/Vpp – External Access: If this pin is grounded the program written in external ROM will be executed. If the EA pin is connected to Vcc, the microcontroller will use both memories, first internal then external (if external exists).
Pin 32-39: Port 0 Similar to P2, if external memory is not used, these pins can be used as general inputs/outputs. Otherwise, P0 is configured as address output (A0-A7) when the ALE pin is driven high (1) or as data output (Data Bus) when the ALE pin is driven low (0).
Pin 40: VCC +5V power supply.

## Slide 75: Oscillator and clock of 8051

## Slide 76: Reset

## Slide 77: Reset
8051 can be reset in two ways 1) is power-on reset – which resets the 8051 when power is turned ON and 2) manual reset – in which a reset happens only when a push button is pressed manually.
Power-On Reset
Initially charging of capacitor makes RST High
When capacitor charges fully it blocks DC.

## Slide 78: Manual reset
Closing the switch momentarily will make RST High.
A reset doesn’t affect contents of internal RAM. For reset to happen, the reset input pin (pin 9) must be active high for atleast 2 machine cycles. During a reset operation :- Program counter is cleared and it starts from 0000H, register bank0 is selected as default, Stack pointer is initialized to 07H, all ports are written with FFH.

## Slide 79: I/O ports
Each port has a D-type output latch for each pin.
The SFR for each port is made up of these eight latches; which can be, addressed at the SFR address for that port.
For example, the eight latches for port 0, can be addressed at location 80h; these are also bit addressable.
The port latches should not be confused with the port pins
The data on the latches need not be the same as that on the pins.
Two data paths are shown in Figure; upper buffer is enabled when latch data is read, and lower buffer is enabled when pin is read.
Different opcodes access the latch or pin states as appropriate.

## Slide 80: PORT1 Structure

## Slide 81: Port 1 Structure
Port 1 pins have no dual functions.
Therefore, the output latch is connected directly to the gate of the lower FET.
This port has an FET circuit labeled Internal FET Pull-up as an active pull-up load.

## Slide 82: Port 0 Structure

## Slide 83: Port 0 Structure

## Slide 84: Port 0 Structure
Port 0 pins may serve as inputs, outputs or, when used together, as a bi-directional low-order address and data bus (AD0-AD7)for external memory.
When a pin is to be used as an input, a 1 must be written to the corresponding port 0 latch by the program,
It turns both of the output transistors off, causes the pin to "float" in a high-impedance state. The pin is connected to the input buffer.

## Slide 85: Port 0 Structure
When used as an output, the pin latches that are programmed to a 0 will turn on the lower FET grounding the pin.
All latches that are programmed to a 1 still float; thus, external pullup resistors will be needed to supply a logic high when using port 0 as an output.

## Slide 86: Port 0 Structure
When port 0 is used as address bus to access external memory, internal control signals switch the address lines to the gates of the Field effect Transistors(FETs).
A logic 1 on an address bit will turn the upper FET on and the lower FET off to provide a logic high at the pin.
When the address bit is a zero, the lower FET is on and the upper FET off to provide a logic ‘0’ at the pin.

## Slide 87: Port 0 Structure
After the address has been formed and latched into external circuits by the Address Latch Enable (ALE) pulse, the bus is turned around to become a data bus.
Port 0 now reads data from the external memory and must be configured as input, so logic 1 is automatically written by internal control logic to all port 0 latches.

## Slide 88: Port 2 Structure
Port 2 may be used as an input/output port similar in operation to port 1.The alternate use of port2 is to supply high-order address byte to address external memory.
Port2 latches remain stable when external memory is addressed, as they do not have to be turned around for data input as is the case for port 0.

## Slide 90: Port 3 Structure
Port 3 is an input/output port similar to port 1. The input and output functions can be programmed under the control of the p3 latches or under the control of various other special function registers.

## Slide 91: Port 3 Structure

## Slide 92: Port 3 Structure
The port 3 alternate uses are shown in the following table:

## Slide 93: P1-P3 operation
When used as an input, a 1 is written to the latch, turning the lower FET off; the pin and the input to the pin buffer are pulled high by the FET load. An external circuit can overcome the high-impedance pullup and drive the pin low to input a 0 or leave the input high for a 1.
Reading the i/p pin
  1. ‘1’ is written to the port latch. The D latch has 1 on its Q o/p and 0 on its Q output
  2. Lower transistor M1 is turned OFF
  3. i/p pin is connected to tristate buffer (TB1)( and is pulled high by internal FET pull up)
  4. Instruction ( eg MOV A,P1) reads data present at the pin ( if i/p is ‘0’ external circuits ground the pin, if not the pin remains at logic ‘1’)

## Slide 94: P1-P3 operation
If used as an output, the latches containing a 1 can drive the pin high through the pullup. If a 0 is written to the latch, the lower FET is on, the pullup is off, and the pin is driven low.
Writing ‘1’ to the o/p pin
  1. ‘1’ is written to the port.
  2. Lower transistor M1 is turned OFF
  3. pin is pulled high by internal FET pull up

## Slide 95: P1-P3 operation
Writing ‘0’ to the o/p pin
  1. ‘0’ is written to the port.
  2. Lower transistor M1 is turned ON
  3. pin is connected to the ground
While executing read modify write instructions port latch is read ( not pin)
Reading latch
  1. Upper buffer (TB2) is enabled
  2. Operation specified by the instruction is performed
  3. Result is written to the latch

## Slide 96: MICROCONTROLLER INSTRUCTION SET

## Slide 97: INTRODUCTION
An instruction is an order or command given to a processor by a computer program. All commands are known as instruction set and set of instructions is known as program.
8051 have in total 111 instructions, i.e. 111 different words available for program writing.

## Slide 98: Types Of Instructions
One/single byte instructions :
If operand is not given in the instruction or there is no digits present with instruction, the instructions can be completely represented in one byte opcode.
OPCODE 8 bit

## Slide 99: Types Of Instructions
Two/double byte instruction:
If 8 bit number is given as operand in the instruction, the such instructions can be completed represented in two bytes.
First byte OPCODE
Second byte 8 bit data or I/O port

## Slide 100: Types Of Instructions
Three/triple byte instruction:
If 16 bit number is given as operand in the instructions than such instructions can be completely represented in three bytes 16 bit number specified may be data or address.

## Slide 101: Types Of Instructions
1. First byte will be instruction code.
2. Second byte will be 8 LSB’s of 16 bit number.
3. Third byte will be 8 MSB’s of 16 bit number.
First byte OPCODE.
Second byte 8 LSB’s of data/address.
Third byte 8 MSB’S of data/address.

## Slide 102: Description of all 8051 instructions
Here is a list of the operands and their meanings:
A - accumulator Rn - is one of working registers (R0-R7) in the currently active RAM memory bank
Direct - is any 8-bit address register of RAM. It can be any general-purpose register or a SFR (I/O port, control register etc.)
@Ri - is indirect internal or external RAM location addressed by register R0 or R1
#data - is an 8-bit constant included in instruction (0-255)
#data16 - is a 16-bit constant included as bytes 2 and 3 in instruction (0- 65535)
addr16 - is a 16-bit address. May be anywhere within 64KB of program memory.
C - is carry flag of the status register (register PSW).

## Slide 103: INSTRUCTION SET
Classified as follows:
    Data transfer instructions
    Arithmetic instructions
    Logical instructions
    Branch instructions
    Subroutine instructions
    Bit manipulation instructions

## Slide 104: 1.Data transfer instructions
In this group instructions perform data transfer operations
Syntax: Mov Destination,Source
Examples: If Rn =R3
MOV A,Rn // move contents of a register to Acc R3=05, A=05
MOV Rn,A // move contents of Acc to register A=05, R3=05
MOV A,#45H // move data 45 to Acc A=45
MOV Rn,# 0AH // move data 0A to a register R3=0A
MOV A,65H // move data at RAM location 65 to Acc
03
65
A=03

## Slide 105: 1.Data transfer instructions
MOV A,@Ri // move data at RAM location addressed by a register to Acc
(R0 & R1 can only be used)
If R1=65H
@ means “content of”
MOV Rn,65H // move data at RAM location 65 to Register ; R3=03
MOV 45H,Rn // move data at Register to RAM location 45; R3=06,
MOV 47H,65H // move data at RAM location 65 to RAM location 47
06
45
03
47

## Slide 106
MOV 45H,@Ri // move data at RAM location addressed by a register to RAM location 45 (R0 & R1 can only be used)
If R1=65H ; Ans
MOVX A,@Ri // Copy the contents of external address in Ri to Acc.This copies the data from the 8 bit address in Ri to Acc
(R0 & R1 can only be used)
X stands for external Memory
06
45
06
65

## Slide 107
MOVX A,@Dptr // Copies data from the 16 bit address in DPTR to Acc
If Dptr =2500H;
MOVX @Dptr,A // Copies data from Acc to 16 bit address in DPTR
If A=06;
03
2500
A=03
06
2500

## Slide 108: Instructions to Access External ROM/Program Memory
MOVC A, @A + DPTR This copy the contents of the external ROM address formed by adding A and the DPTR, to A.
If DPTR =2500H ; A=06 ; A+DPTR =2506
MOVC A, @A + PC This copy the contents of the external ROM address formed by adding A and the PC, to A.
If PC =2500H ; A=06 ; A+PC =2506
Note: MOVC :- Move Code Memory
03
2506
A=03
03
2506
A=03

## Slide 109: Instructions to Store /Retrieve data To/From Stack Memory
PUSH 6 // Increment SP (SP=SP+1) then, data at RAM location 06 is moved to stack memory addressed by SP
If SP=07H
SP : 08=04
POP 7 // Data at stack memory addressed by SP is moved to RAM location 07 the decrement SP (SP=SP-1)
SP=07
XCH A, Rn // Exchange the data at ACC and register Rn A=04; R3=03
06
04
07
04

## Slide 110: 2.Arithmetic instructions
Addition:
ADD A,#45H // A = A + 45
ADDC A,#0B4H // A = A + 0B4 + Carry Flag content
ADD A,Rn // A = A + Data at Rn
ADDC A,Rn // A = A + Data at Rn + Carry Flag content
ADD A,51H //A = A + Data at RAM location 51
ADDC A,51H // A = A + Data at RAM location 51 + CY Flag

## Slide 111
Subtraction:
SUBB A,#45H // A = A - 45 - CY Flag
SUBB A,Rn // A = A - Data at Rn - CY Flag
SUBB A,51H // A = A - Data at RAM location 51 - CY Flag

## Slide 112
Multiplication:
MUL AB= A*B
Multiplies two 8 bit numbers stored in Accumulator and register B
Lower byte of the result will be stored in accumulator and higher byte of the result will be stored in register B
Division:
DIV AB=A/B
Divides two 8 bit numbers stored in Accumulator and register B
result will be stored in accumulator and remainder will be stored in register B

## Slide 113
Increments:
INC A // A=A+1
INC Rn // Rn=Rn+1
Increments the value of source by 1
If initial value if FFh on incrementing the value will reset to Zero
Decrements:
DEC A // A = A - 1
DEC Rn // Rn = Rn – 1
Decrements the value of source by 1
If initial value if zero on decrementing the value will reset to FFh

## Slide 114: 3.Logical instructions
Logical AND:
ANL A,#Data // A = A and Immediate data
ANL A,Rn // A= A and Data at Rn
Logical OR:
ORL A,#Data // A = A or Immediate data
ORL A,Rn // A= A or Data at Rn
Logical EX-OR:
XRL A,#Data // A = A Ex or Immediate data
XRL A,Rn // A= A Ex or Data at Rn
Logical NOT:
CPL A // Invert all bits in Acc
CPL C // Invert Carry Flag
CPL bit address (Eg :CPL 07) // 07 is the address of 8th bit of first bit addressable memory location. Invert it
Swapping of Accumulator Data:
SWAP A // Swap the upper nibble & lower nibble of A

## Slide 115
Rotate Instructions:
1.RR A
Rotate right the accumulator
Each bit is shifted one location to the right, with bit 0 going to bit 7.
2.RL A
Rotate left the accumulator
Each bit is shifted one location to the left, with bit 7 going to bit 0

## Slide 116
3.RRC A
Rotate right through the carry
Each bit is shifted one location to the right, with bit 0 going into the carry bit in the PSW, while the carry was at goes into bit 7
4.RLC A
Rotate left through the carry.
Each bit is shifted one location to the left, with bit 7 going into the carry bit in the PSW, while the carry goes into bit 0.

## Slide 117: 4.Branch instructions
Two Types:
Unconditional jump instruction
  Upon their execution a jump to a new location from where the program continues execution is executed.
  b) Conditional jump instruction
  A jump to a new program location is executed only if a specified condition is met. Otherwise the program normally proceeds with the next instruction.

## Slide 118
The unconditional jump is a jump in which control is transferred unconditionally to the target location
LJMP (long jump)
  3-byte instruction
    First byte is the opcode
    Second and third bytes represent the 16-bit target address
      Any memory location from 0000 to FFFFH
SJMP (short jump)
  2-byte instruction
    First byte is the opcode
    Second byte is the relative target address
      00 to FFH (forward +127 and backward
-128 bytes from the current PC)

## Slide 119
To calculate the target address of a short jump (SJMP, JNC, JZ, DJNZ, etc.)
  The second byte is added to the PC of the instruction immediately below the jump
If the target address is more than -128 to +127 bytes from the address below the short jump instruction
  The assembler will generate an error stating the jump is out of range

## Slide 122: 5.Subroutine instructions
Call instruction is used to call subroutine
  Subroutines are often used to perform tasks that need to be performed frequently
LCALL (long call)
  3-byte instruction
    First byte is the opcode
    Second and third bytes are used for address of target subroutine
– Subroutine is located anywhere within 64K byte address space
ACALL (absolute call)
  2-byte instruction
    11 bits are used for address within 2K-byte range

## Slide 123
When a subroutine is called, control is transferred to that subroutine, the processor
  Saves on the stack the the address of the instruction immediately below the LCALL
  Begins to fetch instructions form the new location
After finishing execution of the subroutine
  The instruction RET transfers control back to the caller
    Every subroutine needs RET as the last instruction

## Slide 125
The only difference between ACALL
and LCALL is
  The target address for LCALL can be anywhere within the 64K byte address
  The target address of ACALL must be within a 2K-byte range
The use of ACALL instead of LCALL can save a number of bytes of program ROM space

## Slide 126: Addressing Modes
  ADDRESSING MODES
The method of specifying the data to be operated by the instruction is called addressing
8051 addressing modes are classified as follows.
  Immediate addressing.
  Register addressing.
  Direct addressing.
  Indirect addressing.
  Indexed addressing

## Slide 127: Addressing Modes
Immediate addressing.
  In this addressing mode the data is provided as a part of instruction itself.
  In other words data immediately follows the instruction.
Eg. MOV A,#30H It means that immediate data 30h provided in instruction is moved into A register.
ADD A, #83 It means that immediate data 30h provided in instruction is added with A register.
# Symbol indicates the data is immediate.

## Slide 128
Register addressing.
  In this addressing mode the register will hold the data.
  One of the eight general registers (R0 to R7) can be used and specified as the operand.
Eg. MOV A,R0 Content of R0 register is copied into Accumulator.
ADD A,R6 Content of R0 register is added with Accumulator.
R0 – R7 will be selected from the current selection of register bank. The default register bank will be bank 0.
Addressing Modes

## Slide 129
Direct addressing
  In this mode the direct address of memory location is provided in instruction to fetch the operand.
  Only internal RAM and SFR's address can be used in this type of instruction.
  Ex: MOV A, 30H => Content of RAM address 30H is copied into Accumulator.
Addressing Modes

## Slide 130
Indirect addressing
  Here the address of memory location is indirectly provided by a register.
  The '@' sign indicates that the register holds the address of memory location i.e. fetch the content of memory location whose address is stored in register.
Ex: MOV A,@R0 => Copy the content of memory location whose address is given in R0 register.
Addressing Modes

## Slide 131
Indexed addressing
  This addressing mode is basically used for accessing data from look up table.
  Here the address of memory is indexed i.e. added to form the actual address of memory.
Ex: MOVC A, @A+DPTR => here 'C' means Code. Here the content of A register is added with content of DPTR and the resultant is the address of memory location from where the data is copied to A register.
Addressing Modes