## Slide 1: ADC/DAC
Melvin C Jose

## Slide 2: Interfacing ADC

## Slide 3: Interfacing ADC
CS: chip select – must be low to access ADC chip
RD: Digital o/p becomes available when H to L pulse is applied
WR: Conversion process starts when a L to H pulse is applied
INTR: Goes low when conversion is finished
CLK IN and CLK R: CLK IN is used to connect external clock. If internal clock is used f=1/(1.1 RC)
Vin (+) and Vin (-): These are the differential analog inputs
Vcc: This is the +5 volt power supply.

## Slide 4: Interfacing ADC
Vref/2: If this pin is open (not connected), the analog input voltage for the ADC0804 is in the range of 0 to 5 volts (the same as the Vcc pin).
Vref/2 is used to implement analog input voltages other than 0 to 5 V. For example, if the analog input range needs to be 0 to 4 volts, Vref/2 is connected to 2 volts.
DO-D7: DO – D7 (D7 is the MSB) are the digital data output pins step size (resolution) is the smallest change, which is (2 x Vref/2)/256 for ADC0804

## Slide 5: Interfacing ADC

## Slide 6: Procedure for ADC interfacing
CS=0
L to H on WR
Monitor INTR.
If INTR low
make CS=0 ,
H to L on RD

## Slide 7: Interfacing Diagram of ADC

## Slide 8: Interfacing Program of ADC

## Slide 9: Interfacing Program of ADC
#include<reg51.h>
#define input P1 //Input port (read values of ADC)
Void delay(unsigned int msec );
Void adc();
Sbit wr= P3^5; // Write pin.
Sbit rd= P3^6; // Read pin.
Sbit intr= P3^4; // Interrupt pin.

## Slide 10: Interfacing Program of ADC
void main()
{
input=0xff; // Declare port 1 as input port.
while(1)
{
adc();
}
}
void delay(unsigned int msec ) // Delay function
{
Int i, j ;
for(i=0;i<msec;i++)
for(j=0; j<1275; j++);
}

## Slide 11: Interfacing Program of ADC
Void adc() // Reading values from ADC
wr=0;
delay(10);
wr=1;
while(intr==1);
rd=0;
A=input;
delay(10);
rd=1;
}

## Slide 12: Interfacing DAC
The digital-to-analog converter (DAC) is a device used to convert digital pulses to analog signals.
DAC0808 uses the R/2R method for digital to analog conversion since it can achieve a much higher degree of precision.
The number of data bit inputs decides the resolution of the DAC since the number of analog output levels is equal to 2n, where n is the number of data bit inputs.
The DAC0808 is an 8 i/p DAC which provides 256 discrete voltage (or current) levels of output.

## Slide 13: Interfacing DAC
In the MC1408 (DAC0808), the digital inputs are converted to current (Iout), and by connecting a resistor to the Iout pin, we convert the result to voltage.
The total current provided by the Iout pin is a function of the binary numbers at the DO – D7 inputs of the DAC0808 and the reference current (I ref), and is as follows:
Where DO is the LSB, D7 is the MSB for the inputs, and Iref is the input current that must be applied to pin 14. The Iref current is generally set to 2.0 mA. Figure shows the generation of current reference (setting Iref = 2 mA) by using the standard 5-V power supply and IK and 1.5K-ohm standard resistors. Now assuming that Iref = 2 mA, if all the inputs to the DAC are high, the maximum output current is 1.99 mA

## Slide 14: Interfacing DAC

## Slide 15: Interfacing DAC

## Slide 16: Using DAC generate a stair-step ramp

## Slide 17: Using DAC generate a stair-step ramp
# include <reg51.h>
void delay(unsigned int msec )
void main(void)
unsigned char d;
while(1)
{
for(d=0x00;d<=0xFF;d++) // send values 00 to FF
{
P1=d; // one by one for positive ramp
MSDelay(100);
}
}
void delay(unsigned int msec ) // Delay function
{
Int i, j ;
for(i=0;i<msec;i++)
for(j=0; j<1275; j++);
}

## Slide 18: Using DAC generate a Sine Wave

## Slide 19: Using DAC generate a Sine Wave
#include<reg51.h>
void main()
{
unsigned char sin_value[] = {128,192,238,255,238,192,128,64,17,0,17,64};
unsigned char i;
while(1)
{
for(i = 0; i<12; i++)
{
P0 = sin_value[i];
}
}
}

## Slide 20: Using DAC generate a Square wave
# include <reg51>
void main(void)
{
while(1)
{
P1=0xFF; // first send all high to P1
MSDelay(100);
P1=0x00; // then send all low to P1
MSDelay(100);
}
}

## Slide 21: Using DAC generate a Triangular wave
# include <reg51>
void main(void)
unsigned char d;
while(1)
{
for(d=0x00;d<0xFF;d++) // send values 00 to FF
{
P1=d; // one by one for positive ramp
}
for(d=0xFF;d>0x00;d--) // send values FF to 00
{
P1=d; // one by one for negative ramp
}
}